Homework Set 13: The Mechanical-Electrical Connection

Due Monday, October 25, 2021

Problems From MT3 (Not in TM5 …  text from MT3 on T :\O’Donoghue\Mechanics\ClassNotes) .

1) 3-22  Show that for an RLC circuit in which the resistance is small, the logarithmic decrement of the oscillations is approximately                  . The logarithmic decerement is defined on p. 111 of TM5.

2) 3-23  Compute the oscillation frequencies, periods and amplitude after 2 periods (as a fraction of A0) for the circuit shown for L = 0.01 H, C = 10 (F, and R = 10 (.

3) 3-24  An electrical circuit consists of a resistor R and a capacitor C connected in series to a source of alternating emf.  Find expressions for the charge and current as a function of time and show that the current decreases to zero  as the frequency of the alternating emf approaches zero.

Solve a differential equation similar to that in Example 3.5 (above Figure 3-18 on p. 125).  Guess a solution that is a sum of a cosine and a sine, then force it to work … look back at how we solved the driven harmonic oscillator … but use Q(t) = Acos((Dt) + Bsin((Dt).  I get (for the last part, expand the cosine and sine in I(t) and assume (D2(0),