The Radiometer Equation

After Chat Hull, UC Berkeley

(www.youtube.com/watch?v=dwT-tMoscsY & casper.berkeley.edu/astrobaki/index.php/Radiometer_Equation_Applied_to_Telescopes)

The radiometer equation, for a bandwidth of (( (MHz) and integration time, ( is

Deriving the Radiometer Equation

Radio astronomers use temperatures because they began as engineers who think about resistors that heat up when you put power through tem.  Change the temperature to fluxes using the Rayleigh-Jeans expression for specific intensity:

The flux density is just the intensity integrated over the solid angle of the sky seen by the antenna, (a,

Where 1 Jy = 10-23 erg/s(cm2(Hz.  The power received by the antenna is the intensity integrated over the effective area of the antenna, Ae, and the solid angle of the sky seen by the antenna, (a.

The antenna theorem states that the effective area of the antenna, times the solid angle it subtends is equal to the observed wavelength squared.

Thus,

To derive the conversion from the source temperature to the flux density of an unresolved source, write the power in terms of the flux density,

Where the factor, Ae/2k is known as the forward gain of the antenna in K/Jy or Jy/K.

The effective area, in terms of the peak antenna gain is defined as

Back to the signal-to-noise, The system temperature is a combination of the sky (eg. noise generated above antenna that we don’t want to detect such as our own galaxy, nearby sources, CBR, etc.) temperature and the temperature of the receiver, the thermal (or Johnson) noise of the electrical components of the receiver:

And, typically Tsrc < Tsys.  To detect objects, we need to beat down the noise which is defined as Trms and is given by

where n is the number of data points, equal to the bandwidth times the integration time:

The signal-to-noise ratio, then is

which is what we set out to derive!

Radiometer Equation in terms of Flux Density

Define the System Equivalent Flux Density (SEFD ~ Jy) as the flux density equivalent of Tsys, found by rearranging (6) to

and write the rms flux density variations (instead of rms system temperature variations) is then

showing that increasing the integration time decreases the flux density of the noise.   The parameters used in these equations are available for the Arecibo receivers in An Astronomer’s Guide to the Arecibo 305-m Telescope by Chris Salter at www.naic.edu/~astro/guide.

# Footnotes

Antennna-Theory.com (www.antenna-theory.com)

# Text boxes

(1)

(2)

(3)

(4)

(5)

(6)

(7)